## Slide 1: Plasterboard
The Essential Ingredients to Safer Handling

## Slide 2
> Plan
Check:
Access into the work area is clear and prepared
Plasterboard is weather protected
Plot has been cleaned out
Dimensions are accurate

## Slide 3
> Plan
Check:
Ceiling noggins are present to carry the boards
How will the boards be moved?
Is any plant or assistance required – team lifting
Stairwell protection is in place

## Slide 4
> Deliver
Check:
Forklift has loaded out at the right angle leaving space to load into the plot.
Laydown area is clear and free of tripping hazards.

## Slide 5
> Deliver
Check:
Access into the plot is ramped where there is a step up from ground level.
Scaffolding has been adapted to provide clear access.

## Slide 6
> Move
Use:
Good handling techniques – consider team lifting
Letterbox openings to load out upper floors

## Slide 7
> Stack
Stack:
On its side against a wall at an angle, or flat on its back for stability
Limit number of boards for stability to avoid overloading & ‘suction effect’

## Slide 8
> Fix
Use:
Two man lifting above head height or a proprietary lifter
Sharp knife – regularly change blades, consider gloves
Proprietary hop ups with a suitable safe working load displayed

## Slide 9
> Fix
Use:
Proprietary working platform when boarding in stairwells
Ensure that the equipment is suitable for the opening